## Slide 1: CHEEREIO: a generalized, open-source ensemble-based chemical data assimilation and emissions inversion platform for the GEOS-Chem chemical transport model
10 November 2022 13th GEMS workshop
Drew Pendergrass
with Daniel Jacob, Hannah Nesser, Daniel Varon, Melissa Sulprizio, Kazuyuki Miyazaki, and Kevin W. Bowman

## Slide 2: Table of contents
What CHEEREIO is and how it works
Example applications: CH4 and NOx inversions
Why CHEEREIO makes it easy to do inversions

## Slide 3: Table of contents
What CHEEREIO is and how it works
Example applications: CH4 and NOx inversions
Why CHEEREIO makes it easy to do inversions

## Slide 4: Data assimilation allows atmospheric models to incorporate observations
Anthropogenic and biogenic
emissions
Sunlight
Aerosols
and clouds
CHEMISTRY
Transport
Deposition
Remote sensing
Surface monitoring
Predict
Observe
Assimilate
Emissions and chemistry
corrected to match reality
CHEEREIO

## Slide 5: There are many approaches to assimilation and emissions correction
Variational approaches iteratively approximate optimal solution…
…but 4D-Var requires adjoint; harder to work with most recent GC chemistry
The analytical inversion perturbs
clusters of grid cells to obtain full error characterization…
…but requires hundreds of runs, and
works only for linear problems
Sheng et. al., 2018
ECMWF

## Slide 6: CHEEREIO uses ensembles with random emissions to emulate model uncertainty
Time
Concentration
Ensemble of simulations
Observations
Time
Concentration
Base model
Observations
Base error
No data assimilation
With 4D-LETKF
Use observations to update emissions and concentrations over time

## Slide 7: Summary of CHEEREIO project goals
Customization: Assimilate anything, in any GEOS-Chem configuration or simulation.
Powerful API: Minimal programming required for new simulations
Easy deployment: One configuration file controls installation and settings
Maintainability: Science automatically aligned with latest model version

## Slide 8: Table of contents
What CHEEREIO is and how it works
Example applications: CH4 and NOx inversions
Why CHEEREIO makes it easy to do inversions

## Slide 9: Applications currently under development
Data on disk
HEMCO
Observations
Model state
Emissions
Optimize global NOx emissions
OMI NO2 columns
Species in NOx mechanism
NOx scaling factors
CHEEREIO
Simultaneously optimized NOx
scaling factors and concentrations
Data on disk
HEMCO
Observations
Model state
Emissions
Optimize global CH4 emissions
TROPOMI CH4 columns
CH4
CH4 scaling factors
CHEEREIO
Simultaneously optimized CH4
scaling factors and concentrations

## Slide 10: Evolution of CH4 emissions scaling factors through assimilation
Assimilate every 7 days for one year (2019), with two months of burn-in assimilation discarded

## Slide 11: Assimilated results against observations, adjusted OH fields
-

## Slide 12: Applications currently under development
Data on disk
HEMCO
Observations
Model state
Emissions
Optimize global NOx emissions
OMI NO2 columns and
surface data
Species in NOx mechanism
NOx scaling factors
CHEEREIO
Simultaneously optimized NOx
scaling factors and concentrations
Data on disk
HEMCO
Observations
Model state
Emissions
Optimize global CH4 emissions
TROPOMI CH4 columns
CH4
CH4 scaling factors
CHEEREIO
Simultaneously optimized CH4
scaling factors and concentrations

## Slide 13: Evolution of NOx scaling factors through last two weeks of January 2016
Assimilate every 24 hours for two weeks (January 15-31, 2016)
Notes: Had to average prior and posterior and limit scaling factor update to 50% to prevent scaling factors from jumping negative from a weird observation. Working to add more filters to protect against this.

## Slide 14: Comparison with prior
Δ (PRIOR – TROPOMI)
Δ (POSTERIOR – TROPOMI)

## Slide 15: Table of contents
What CHEEREIO is and how it works
Example applications: CH4 and NOx inversions
Why CHEEREIO makes it easy to do inversions

## Slide 16: Assemble the building blocks of your simulation in the configuration file
Group emissions into families
From one file…
ens_config.json
NO2
NO
HNO3
Select concentrations in your state vector…
…and how they are defined.
Surface
Column sum
Tropospheric column
Define emissions in your state vector…
NOx
NO
NO2
Separate sectors for source attribution
Transport NOx
Industrial NOx
…and specify uncertainties.
Combine the observations you want to use…
…and customize filters and aggregation.
OMI
TROPOMI
GEMS
Surface obs.
Customize!
CHEEREIO puts the pieces together!

## Slide 17: Add new observation operators easily with Python-based inheritance
CHEEREIO is assembled from interchangeable blocks
Observation operators go here
CHEEREIO provides a template for observation operators…

## Slide 18: Add new observation operators easily with Python-based inheritance
CHEEREIO is assembled from interchangeable blocks
CHEEREIO provides a template for observation operators…
…that then automatically plug in to the CHEEREIO workflow
OMI
TROPOMI
GEMS
Surface
Add your own!
GEMS inversion ready to go!

## Slide 19: The CHEEREIO workflow
Run GC until
assimilation
time
Emissions, boundary conditions, and meteorology on disk
ens_config.json
Create template run directory
(User modifies as necessary)
Spinup run(s)
Sample prior distribution of
scaling factors
Initial
conditions
N ensemble members
N ensemble members
N ensemble members
Observations on disk
Wrap GEOS-Chem output, scaling factors, and observations in Python objects
GEOS-Chem/CHEEREIO model pipeline
Produce user-defined state vector containing relevant emissions and concentrations
Run assimilation algorithm (LETKF)
Apply post-assimilation corrections
CHEEREIO assimilation pipeline
Gather posterior concentrations and emissions
Simulate modeled observations (e.g. with averaging kernel)
No modifications of model code!!

## Slide 20: Postprocessing tools consolidate data and automatically produce hundreds of customizable animations and plots
All plots and movies shown previously were auto-generated by CHEEREIO!

## Slide 21: CHEEREIO is documented on ReadTheDocs for ease-of-use, with lots of examples!
bit.ly/CheereioDocs

## Slide 22: Why you should use CHEEREIO for GEMS
CHEEREIO makes it easy to do any inversion!
Quickly run multiconstituent inversions with GEMS
Combine GEMS with surface observations and other satellite instruments
Spend your time on science, not software engineering
NO2
O3
HCHO
OMI
TROPOMI
GEMS
Surface obs.
Customize!
Notes: 1) Cheereio almost ready! You should use it! It makes inversions as easy as they can be. I went from no NOx inversion, no operator, to running six different inversions in about a month.

## Slide 23: Thank you! Questions?
Drew Pendergrass (pendergrass@g.harvard.edu)
Download and use* the code
Read the documentation
*Official release and model description paper coming soon!
bit.ly/cheereio
bit.ly/CheereioDocs

## Slide 24: Extra slides

## Slide 25: Current issues with the methane inversion
Prior error too small
Not enough burn-in time
Jan
Mar
May
Jul
Sep
Nov
Month of 2019
Jan
Mar
May
Jul
Sep
Nov
Month of 2019
Notes: Xuan Wang’s Cl fields won’t run (causes crash). Further tuning of parameters necessary. Some sort of spread amplifier would be useful.
Want to deploy to cloud for NRT application soon.