## Slide 1: Running CHEEREIO 1.3 A hands-on guide to nonlinear ensemble data assimilation and emissions estimation with GEOS-Chem
11th International GEOS-Chem meeting clinic
Drew Pendergrass
June 10, 2024

## Slide 2: Table of contents
Introduction to ensemble data assimilation and CHEEREIO
Installing CHEEREIO and building your first ensemble
Selecting or adding observation operators
Running and debugging CHEEREIO
Postprocessing and data analysis tools

## Slide 3: Table of contents
Introduction to ensemble data assimilation and CHEEREIO
Installing CHEEREIO and building your first ensemble
Selecting or adding observation operators
Running and debugging CHEEREIO
Postprocessing and data analysis tools

## Slide 4: The bottom-up method of emissions estimation
Emissions factor
Fuel type, scrubbers, etc.
Vehicle type
Distance traveled
Amount of electricity generated
Activity level
x
=
Emissions
Emissions from electricity
Emissions from transportation
x
x
=
=
+
+
Emissions from other sectors
=
Total emissions
Bottom-up emissions are necessary but imperfect.
Observations can help quantify missing sources.
Notes: Repeat for every pollutant and every source of each pollutant.

## Slide 5: Data assimilation allows atmospheric models to incorporate observations
Anthropogenic and biogenic
emissions
Sunlight
Aerosols
and clouds
CHEMISTRY
Transport
Deposition
Remote sensing
Surface monitoring
Predict
Observe
Assimilate
Emissions and chemistry
corrected to match reality

## Slide 6: CHEEREIO guesses emissions and compares model to observations
… satellite would measure
150 ppb NOx
If we emit 1000 kg NOx per hour…
If we emit 500 kg NOx per hour…
… satellite would measure
75 ppb NOx
Real satellite measures
100 ppb NOx…
… so truth is in between these two guesses

## Slide 7: Ensemble-based approaches are a relatively cheap way to handle linear and non-linear problems
Time
Concentration
Ensemble of simulations
Observations
Time
Concentration
Base model
Observations
Base error
No data assimilation
With Ensemble DA
Information from observations
accumulates with time

## Slide 8: How ensemble chemical data assimilation works
Generate n perturbations
to initial emissions
…
Run a CTM for each
emission field
…
Generate n simulated 3D atmospheres, each reflecting different emissions
Apply observation operators (e.g. satellite averaging kernels)
Compare simulated observations to actual observations
…
…
Use ensemble spread to approximate prior error covariance matrix
Specify or calculate observational error covariance matrix

## Slide 9: How ensemble chemical data assimilation works
Weighting by covariance matrices, calculate optimal posterior emissions and/or concentrations
…
…
Generate n simulated 3D atmospheres, each reflecting different emissions
Apply observation operators (e.g. satellite averaging kernels)
Compare simulated observations to actual observations
…
…
Use ensemble spread to approximate prior error covariance matrix
Specify or calculate observational error covariance matrix
Run a CTM for each
emission field
Rinse and repeat

## Slide 10: There are many other approaches to assimilation and emissions correction
ECMWF
Variational approaches iteratively approximate optimal solution…
…but 4D-Var requires GEOS-Chem adjoint, which may not be ideal for some problems
The analytical inversion perturbs
clusters of grid cells to obtain full error characterization…
…but requires hundreds of runs, and
works only for linear problems
Sheng et. al., 2018

## Slide 11: CHEEREIO makes ensemble data assimilation as easy as running GEOS-Chem across many species/observers
Customization: Assimilate anything, in any GEOS-Chem configuration or simulation.
Powerful API: Minimal programming to implement any experiment
Easy deployment: One configuration file controls installation and settings
Maintainability: Science automatically aligned with latest model version
Speed: Runs slower, but not an order of magnitude slower, than GEOS-Chem classic

## Slide 12: Assemble the building blocks of your simulation in the configuration file
Group emissions into families
From one file…
ens_config.json
NO2
NO
HNO3
Select concentrations in your state vector…
…and how they are defined.
Surface
Column sum
Tropospheric column
Define emissions in your state vector…
NOx
NO
NO2
Separate sectors for source attribution
Transport NOx
Industrial NOx
…and specify uncertainties.
Combine the observations you want to use…
…and customize filters and aggregation.
OMI
TROPOMI
GEMS
Surface obs.
Customize!
CHEEREIO puts the pieces together!

## Slide 13: CHEEREIO supports many customizations: aggregating into super-observations
Chen et al., 2023
Same background  correlated retrieval errors

## Slide 14: Table of contents
Introduction to ensemble data assimilation and CHEEREIO
Installing CHEEREIO and building your first ensemble
Selecting or adding observation operators
Running and debugging CHEEREIO
Postprocessing and data analysis tools

## Slide 15: Getting ready: detailed documentation is provided on ReadTheDocs
All the material discussed today and much more is covered in the CHEEREIO documentation, available at bit.ly/CheereioDocs

## Slide 16: Getting ready: frequently asked questions
How hard is it to run CHEEREIO?
  If your system is set up to run GEOS-Chem Classic, it can run CHEEREIO with a few very minor modifications. User experience is also similar to running GC.
What input data is required for CHEEREIO?
  Same as GEOS-Chem Classic, plus whatever observational data you would like to assimilate (e.g. satellite datasets).
What compute resources are required for CHEEREIO?
  A cluster is necessary. CHEEREIO involves running an ensemble of ~16-64 GEOS-Chem runs. Because the calculation is embarrassingly parallel, these runs can be on different nodes or even different partitions (no MPI). Options are available to trade off cores/memory for speed.

## Slide 17: Getting ready: using git to obtain source code
Clone the CHEEREIO repository from GitHub: git clone git@github.com:drewpendergrass/CHEEREIO.git
If you want a CHEEREIO version before the latest release, check out now: git checkout -b NewBranch tags/v1.3.1
Clone the GEOS-Chem Classic repository inside CHEEREIO, or copy GCClassic repo already downloaded.
  git clone --recurse-submodules https://github.com/geoschem/GCClassic.git GCClassic
  This folder must be named GCClassic.

## Slide 18: A tour of the CHEEREIO top-level code directory

## Slide 19: Getting ready: setting up software environments
Requirements: GEOS-Chem Classic 13/14 environment, plus
Python as managed by Anaconda or Mamba
jq
Ultra lightweight JSON library for shell. Most clusters have it installed as a module
Parallel
Standard lightweight shell-level parallelization library. Most clusters have it installed as a module

## Slide 20: Getting ready: setting up software environments
Environment file
Conda environments
Modify environments > cheereio.env for your system
Install cheereio and animation conda environments (environments > cheereio.yaml and > animation.yml)
Command likely will look like the following:
conda env create -f cheereio.yaml
OR
mamba env create -f cheereio.yaml
Modify CondaEnv and AnimationEnv fields in ens_config.json to match installed environment names (cheereio and animation by default).

## Slide 21: Initialization: defining ensemble settings
Ens_config.json supersedes the normal GEOS-Chem run directory creation process.
At the top of the file, you specify your GEOS-Chem settings

## Slide 22: Initialization: defining ensemble settings
Beyond normal spinup, LETKF requires ensemble spinup — time for emissions differences between ensemble members to be realized in concentration spreads.
Concentration
Ensemble of simulations, all starting from same restart
First observations
(Optional) Scale initial ensemble mean to match observation mean
Ensemble spinup
LETKF begins

## Slide 23: Initialization: defining ensemble settings
Define state vectors

## Slide 24: Initialization: deploying the ensemble
Activate cheereio shell environment
In setup_ensemble.sh turn on Template Run directory creation only
Execute script, then navigate to MY_PATH/RUN_NAME
Copy of code used to run ensemble
Ensemble GC run directories
Postprocessed output files
Temporary files, runtime status
Template GC run directory

## Slide 25: Initialization: deploying the ensemble
Edit template run directory. Settings will be repeated across the ensemble.
CHEEREIO automatically edits HEMCO_Config to link emissions to LETKF scale factors

## Slide 26: Initialization: deploying the ensemble
Return to setup_ensemble.sh
In setup_ensemble.sh turn off Template Run directory creation and turn on compilation and setup ensemble runs.
Execute. We are now ready to run the ensemble!

## Slide 27: Table of contents
Introduction to ensemble data assimilation and CHEEREIO
Installing CHEEREIO and building your first ensemble
Selecting or adding observation operators
Running and debugging CHEEREIO
Postprocessing and data analysis tools

## Slide 28: Add new observation operators easily with Python-based inheritance
CHEEREIO is assembled from interchangeable blocks
Observation operators go here
CHEEREIO provides a template for observation operators…

## Slide 29: Add new observation operators easily with Python-based inheritance
CHEEREIO is assembled from interchangeable blocks
CHEEREIO provides a template for observation operators…
…that then automatically plug in to the CHEEREIO workflow
OMI
TROPOMI
GEMS
Surface
Add your own!
GEMS inversion ready to go!

## Slide 30: Automatically validate results with other observers within one workflow
Within the configuration file…
…turn on two observers of one species (CH4)…
TROPOMI
Surface
…turn on TROPOMI for LETKF updates
…but use ObsPack as an independent validation set (no assimilation)
Notes: What’s great about this is that any CHEEREIO observation operator can automatically be used to validate a run, no programming required.

## Slide 31: Anatomy of a CHEEREIO observation operator
A Python class which inherits the CHEEREIO Observation Translator parent class — templating
(Optional) Utility method that links observer dates to files — speeds up CHEEREIO
(Optional) Obspack-specific method which finds files with observations between two dates

## Slide 32
Anatomy of a CHEEREIO observation operator
Function which loads observation data and saves to a standardized dictionary.
CHEEREIO requires 1D arrays for observer value, longitude, latitude, and utctime. All other fields are optional.
MANDATORY FUNCTION 1
Requires species key (references observed species in ens_config) and time period.

## Slide 33
Anatomy of a CHEEREIO observation operator
MANDATORY FUNCTION 2
Core observation operator which compares GEOS-Chem and observations.
Data is returned in ObsData class, which is a list of 1D arrays where GEOS-Chem data are aligned

## Slide 34
Anatomy of a CHEEREIO observation operator
CHEEREIO knows to look for your observation operator because of the operators.json file in top-level directory
ens_config.json
operators.json
Looks inside core/tropomi_tools.py
Finds the TROPOMI_Translator class

## Slide 35: Table of contents
Introduction to ensemble data assimilation and CHEEREIO
Installing CHEEREIO and building your first ensemble
Selecting or adding observation operators
Running and debugging CHEEREIO
Postprocessing and data analysis tools

## Slide 36: Run time: executing the ensemble
(1) Execute nohup bash run_ensspin.sh &
(2) Once all runs complete, execute nohup bash run_ens.sh &

## Slide 37: CHEEREIO runtime: behind the scenes

## Slide 38: Run time: checking ensemble progress, duplication, and backup restoration

## Slide 39: Table of contents
Introduction to ensemble data assimilation and CHEEREIO
Installing CHEEREIO and building your first ensemble
Selecting or adding observation operators
Running and debugging CHEEREIO
Postprocessing and data analysis tools

## Slide 40: Postprocessing: ensemble snapshots and full postprocessing suite
While CHEEREIO is running
Get super-fast view of ensemble status with snapshot.sh

## Slide 41: Postprocessing: ensemble snapshots and full postprocessing suite
After CHEEREIO completes
Get complete set of postprocessing files with postprocess.batch
Total posterior methane emissions
January through May 2019

## Slide 42
Hemco output (full emissions, scale factors applied) follows same conventions
Postprocessing: emissions scaling factors

## Slide 43
Postprocessing: bigY, or observation operator raw output
Entries for every assimilation period

## Slide 44
Postprocessing: bigY, or observation operator raw output
For every date, a table of each ensemble mapped to observations, along with geospatial data and metadata

## Slide 45
Postprocessing: bigY, or observation operator raw output
…
For every date, a table of each ensemble mapped to observations, along with geospatial data and metadata

## Slide 46
Postprocessing: bigY gridded for plotting
GC ensemble mean, mapped to operator, gridded (time,lat,lon)
Observations, averaged to GC grid (time,lat,lon)
Control GC simulation, no assimilation (time,lat,lon)
…

## Slide 47
Useful resources
CHEEREIO paper: https://gmd.copernicus.org/articles/16/4793/2023/
CHEEREIO website: https://cheereio.seas.harvard.edu
CHEEREIO documentation: https://cheereio.readthedocs.io
GEOS-Chem website: https://geoschem.github.io/
Details on GEOS-Chem (and CHEEREIO) software requirements: https://geos-chem.readthedocs.io/en/stable/getting-started/system-req-soft.html
I am here to help! Ask any questions at https://github.com/drewpendergrass/CHEEREIO/issues (preferred) or by email: pendergrass@g.harvard.edu